Standard Construction Features For Phase III Villas

## Quality Construction Traditional Stick frame Construction at Vendors preference.  Note some substitutions of equal quality may apply to below (based on type and season of construction.)

- Poured concrete foundations on poured concrete footings with waterproofing around foundation perimeter

- Standard 7’ 10" basement (Note 1)

- Kiln dried floor joists on 16" centres, with 5/8"tongue and groove plywood sub flooring, glued and pneumatically fastened to ensure a more silent floor.  Steel beam for main support beam.

- 2 x 6 exterior walls built on 16" centres for a quality premium structure.

- Wall and ceilings insulated to meet or exceed the Ontario Building Code SB-12 for Energy Efficiency

(Attic: R60, Walls: R22, Basement R10 continuous insulation board plus R12 batt insulation)

- CGC wall systems between units for sound proofing and fireproofing

- Roof system includes galvanized metal eaves starters on entire perimeter.

- Roof covered with quality Duration asphalt shingles

- Garage includes pre-finished steel sectional doors as per elevations

## Heating

- Natural gas high efficiency forced air heating system with ducting sized to accommodate optional central air conditioning

- Energy efficient Heat Recovery Ventilating System (HRV) installed and balanced to supply a continuous flow of fresh air throughout your home.

- Natural Gas Water Heater (Rental)

## Electrical

- 200 amp underground service with circuit breaker panel

- All copper wiring throughout house

- Light switches and electrical outlet heights are adjusted for ease of use

- Door chimes installed at front entrance way.

- Pre wired for optional garage door opener

- Two exterior GFI plugs, one at back of home and on front porch

- Attractive modern ceiling fixtures (where applicable) all bedrooms, family room, great room, and closets. (As per plans)

- Switch controlled receptacle in living room.

- Pre-wired for two telephone and two cable television outlets (client to choose locations)

- Exterior coach lighting installed at all points of entry.

## Plumbing

- Double stainless steel kitchen sink with single lever faucet

- Opening for dishwasher with plumbing and electrical rough in

- Anti-scald pressure balancing valves in all showers

- Water efficient toilets, taps and shower heads One piece acrylic tub and shower units (as per plan)

- Two exterior taps

- Irrigation system installed front and sides

## Exteriors/Windows and Doors

- Stone skirt to window ledge

- Maintenance free quality vinyl siding, in Board and Batten design, remainder of frontage and three sides in a variety of colours

- Maintenance free aluminum soffit, fascia and eavestroughs

- Maintenance free Low E argon filled vinyl windows throughout with internal colonial grills (as per elevations)

- Maintenance free vinyl basement windows (as per plans) Standard is 48” x 32”

- Maintenance free insulated steel doors complete with vinyl clad frames

## Exterior Features

- Fully graded and sodded lot

- Paved asphalt driveway

- Decorative interlock stone walkway to front entrance from driveway

- All services underground including, telephone, gas, cable and hydro

- Decorative lamp post in front yard

- 8’ x 8’ Pressure treat deck

## Kitchen

- Quality cabinetry with quality cabinet hardware.

- Laminated counter tops in a variety of colour choices

- Two-speed range hood fan with light and charcoal filter.

- Contains one bank of pots and pans roll out drawers for easy access

## Bathroom

- Quality cabinetry with quality hardware

- All fixtures white with chrome bathroom accessories

- Mirrors in all bathrooms installed within six inches of full width of all vanities

## Interior Finishes

- All interior drywall surfaces have two finish coats of interior latex designer white

- Textured ceilings throughout

- 8' ceilings are standard on main living level

- Tray ceiling in Living room and Dining room

- Modern white painted baseboard and window Trim Package

- Modern Interior Doors with modern hardware.   Various upgrade options are available.

- Superior ½" underpad installed under carpet

- Quality Luxury Plank floors throughout Living room, Dining Room and hallways. Bedrooms have carpet in a variety of colour choices.

- Ceramic tile in kitchen, foyer, bathrooms and laundry room in a variety of colours

## Warranty

- Full new Seven Year Home Warranty as per Ontario New Home Warranty Program (Tarion)